## Slide 1: Thoughts on Fugu…

## Slide 2: Spiking algorithms are weird and spiking hardware is weirder
Fugu aims to abstract the task of using spiking neuromorphic hardware for the general CS user
High-level access
  Program in C++ or Python
  Enable heterogeneous solutions
Mid-level algorithms
  Leverage growing library of spiking neural algorithms to
  Link neural algorithms together
Low-level mapping
  Pass application specific neural algorithm to hardware
  Handle I/O between neural and non-neural task components

## Slide 3: Mid-level requirements
What do modules and output algorithms look like?
How do we link SNAs?

## Slide 4: Defining a Fugu Module
Inputs
  Needs to match output of upstream module(s)
  Size (# neurons)
    Does algorithm scale to input size?
  Input time
    Is input all single step? (Tin=1)
    Is input structured over some time range?
xin
Tin

## Slide 5: Defining a Fugu Module
Outputs
  Needs to match input of downstream module(s)
  Size (# neurons)
    How does algorithm scale to output size?
  Output time
    Is output all single step? (Tout=1)
    Is output structured over some time range?
  Delay time – depth of algorithm
    How many time steps does output arise after corresponding input?
    Delay and Input/Output Time are not the same!!!
xout
Tout
xin
Tin
Dout

## Slide 6: Examples
SpikeSort
xin
Tin
xout
Tout
Dout
xin = xout
Tin = 1
Tout = max(xin)
Dout = 1 (2? if buffer holds input?)
SpikeSort begins output relevant information as soon as input arrives; but outputs are temporally extended as network expands input data into time dimension

## Slide 7: Examples
(Strassen) Matrix Multiplication
xin
Tin
xout
Tout
Dout
xin = 2 (NxN matrices, unfolded) – 1x 2N2
xout = 1 x N2
Tin = 1
Tout = 1
Dout = ~7 (depends on version)
Strassen matrix multiply network takes in two input matrices and outputs one output matrix. Inputs and outputs are a single time-step vector. Algorithm takes several time steps to compute through layers, so depth is >1. Depth is related to algorithm size

## Slide 8: Examples
Particle Random Walk Code
xin
Tin
xout
Tout
Dout
xin = k, where k is number of ring neurons, to initialize position
xout = k (output position)
Tin = 1
Tout = 1
Dout = 2*Length of simulation
Particle RW algorithm is entirely parallel – each walker circuit can operate independently of all others. The length of the simulation equates to the depth of the circuit (though the circuit uses feedback). Input and output are just start and final positions

## Slide 9: Examples
…
xin
Tin
xout
Tout
Dout
xin = 2 (NxN matrices, unfolded) – 1x 2N2
xout = 1 x N2
Tin = 1
Tout = 1
Dout = ~7 (depends on version)
Strassen matrix multiply network takes in two input matrices and outputs one output matrix. Inputs and outputs are a single time-step vector. Algorithm takes several time steps to compute through layers, so depth is >1

## Slide 10: Implications
Modules have to match input and output structures
  Size and Time of a module’s outputs must equal the downstream input
Delay has to be accounted for globally
  If information is being processed in parallel, then delays must match

## Slide 11: We can take put SpikeSort at the back-end of Strassen, but not the other way around…
xout
xin = 2 (NxN matrices, unfolded) – 1x 2N2
xout = 1 x N2
Tin = 1
Tout = N2 (?)
Dout = ~7 (Strassen) + 2 (sort)

## Slide 12: Delays need to be accounted for in parallel computation
t=0
t=5
t=10
t=15
t=20
t=25
2
3
t=30
4
1
This mismatch will cause a failure, as module 4 won’t be processing temporally corresponding information as coming out of module 3

## Slide 13: Delays need to be accounted for in parallel computation
t=0
t=5
t=10
t=15
t=20
t=25
2
3
t=30
4
1
Adding a repeater / delay circuit will help coordinate timing of right and left parallel pathways
Delay

## Slide 14: Important to consider control knobs as well - perhaps these are distinct class of I/O
xin
Tin
xout
Tout
Dout
Control knobs for:
  Context modulation
  Timing / synchronization
  Verification of progress / checkpointing?
  Mid-compute visualization
  …

## Slide 15: Examples
Random Walk graph vertex
xin
Tin
xout
Tout
Dout
xin = d, where d = # vertex connections
xout = d
Tin = Nd – max number of walkers from input vertices
Tout = N – number of walkers on vertex
Dout = log2d
Certain algorithms, such as this RW algorithm, will have a non-predetermined output length (it runs until it stops). The use of a supervisor circuit through control connections can help sync components
Start signal from supervisor
Finished signal to supervisor

## Slide 16: To do
We should go through all of our SNAs and identify what this structure looks like
  Is the above description sufficient at a mid-level to facilitate plug-and-play?
  Obviously this lacks some description of coding scheme, but that will be very algorithm dependent.